## Slide 1
eRD6 Progress Report
Kondo Gnanvo
On Behalf of eRD6
EIC GENERIC DETECTOR R&D ADVISORY COMMITTEE MEETING
January 18, 2017

## Slide 2
The eRD6 Consortium
Brookhaven National Laboratory (BNL)
    People: E.C Aschenauer, B. Azmoun, A. Kiselev, M. L. Purschke, C. Woody
    R&D: Mini-Drift detector; TPC/Cherenkov prototype (TPC-C); zigzag pad development.
Florida Institute Of Technology (FIT)
    People: M. Bomberger, M. Hohlmann, F. Izquierdo
    R&D: Large & low mass GEM with zig-zag readout structures.
INFN Trieste
    People: S. Dalla Torre, S. Dasgupta, G. Hamar, S. Levorato, F. Tessarotto
    R&D: Hybrid MPGD for RICH applications.
Stony Brook University (SBU)
  People: K. Dehmelt, A. Deshpande, N. Feege, T. Hemmick
  R&D: Short radiator length RICH; Large mirror coating.
University Of Virginia (UVa)
  People: K. Gnanvo, N. Liyanage
  R&D: Large & low mass GEM with u-v readout; Chromium-GEM (Cr-GEM).
Yale University
  People: D. Majka, N. Smirnov
  R&D: 3-D-coordinate GEM readout; hybrid gain structure.

## Slide 3
2D U-V strip flexible readout & components of double side zebra connection
Progress @ UVa: Large FT GEM Prototype Assembly
U-V strips readout & all pieces for Zebra connection available
All mechanical parts for the double sided zebra procured from CERM
  10 Zebra-to-Panasonic adapter cards &10 zebra holders
Two sets of support frames
Plans for the coming months:
Complete the design and procurement of the low cost frames
Refurbishment of existing Clean Room tools for the assembly
High cost Inner Frames for GEMs with spacer grids
Four Inner Frames with 300 µm spacers grid for GEM foils
Precision machining of PERMAGLAS by RESARM (Belgium)
High material and machining cost
Low Cost Outer Frames without spacer grids
Four Outer Frames for gas window foils without spacers grid
Each frame made of four G10 pieces cut out in local UVa machine shop
Low material and production cost

## Slide 4
Progress @ UVa: Optical Inspection of Chromium GEMs
Optical inspection with GEM CDD Scanner at Temple U.
Scan 2 Cr-GEM foils (one damaged and one good foil)
Outer hole size turns out to be very challenging:
    Poor contrast from the back light transmission
    Poor image resolution
Good uniformity for the inner hole diameter
Hole pitch ~138 µm, 2nd peak at ~141 µm for both foils
  Second peak is more pronounced for the damaged foil
Good foil (Cr-GEM3)
Damaged foil (Cr-GEM1)

## Slide 5
Progress @ UVa: SEM of damaged foil (Cr-GEM1)
SEM images of the top of the damaged Cr-GEM1 foil, as expected, SEM images of top side are good quality with holes dimensions configuration and the cross section view looking normal GEM foil
side here the Cr layer was removed appears severely distorted under SEM
bad image resolution
Cross section of the holes: looks as if the Cr layer melted but the Kapton looks fine
Bottom side
Top side

## Slide 6
Damaged Cr-GEM1 bottom side
SEM without conductive tape
SEM with conductive tape
Distortions are explained by the fact that the SEM measurement was performed on a non metallic surface
Well know issue of charging of dielectric sample when bombarded with the intense SEM beam
  Problem: Charging up disturbs the electric field around the surface under probe ⇨ poor resolution SEM image
  Solution: coating the surface with a thin conductive tape (a few nm of Au) before the SEM measurement
Progress @ UVa: SEM of damaged foil (Cr-GEM1)
Confirmation that the damages in high rate and high gain environment is limited to evaporation of the Cr layer at the the bottom side of the foil
Discussion within the RD51 community suggest that this “evaporation” can be due to heat released during spark or plasma etching process
No issue with the other two Cr-GEMs of the triple GEM ⇨ Hybrid Cr (top) – Cu (bottom) GEM as 3rd GEM for application that requires high rate

## Slide 7
Progress @ UVa: Plans & Milestones
Plans
  Assemble large FT GEM prototype and characterization @ UVa Detector Lab
  Perform tests in beam at the Fermilab Test Beam Facility (FTBF) in July 2018
  Simulation of the impact of material budget on EIC detector (UVa Grad. Student)
  Start testing small 10 cm × 10 cm 2D µRWELL detector (Order of the parts from CERN PCB workshop already processed)
  Start the draft of the paper on Chromium GEMs for submission to NIM A or IEEE TNS
Milestones
  March - April 2018: Assembly of EIC-FT GEM prototype
  Mai 2018 – June 2018: Characterization & performance tests @ UVa with Cosmic, X-rays, Sr90
  June 2018: EIC simulation running @ UVa
  July 2018: Beam tests at Fermilab, Chromium GEM manuscript ready for submission

## Slide 8
eRD6 Publication List: Breakdown per institute
Brookhaven National Lab
“A Study of a Minidrift GEM Tracking Detector”, B. Azmoun et.al., IEEE Transactions on Nuclear Science, Vol. 63, No. 3 (2016) 1768-1776.
“A Prototype TPC/Cherenkov Detector with GEM Readout for Tracking and Particle Identification and its Potential Use at an Electron Ion Collider”, C.Woody et.al., proceedings of the 2015 Micropattern Gas Detector Conference, European Journal of Physics (in press).
“A Study of a Combination TPC-Cherenkov Detector using a CsI Photocathode and GEM Based Readout”, B.Azmoun et.al., in preparation for submission to the IEEE Transactions on Nuclear Science.
A paper entitled “Beam Test results from a Combination TPC-Cherenkov Detector” is currently being prepared for submission to the IEEE journal, Transactions on Nuclear Science in the coming weeks.
Florida Tech
Manuscript in preparation: A. Zhang, M. Hohlmann, B. Azmoun, M. L. Purschke, C. Woody, “A GEM readout with radial zigzag strips and linear charge-sharing response,” to be submitted to Nucl. Inst. Meth. A; presented also as a poster at the 2016 IEEE NSS, Strasbourg, France.
Manuscript in preparation: M. Bomberger, A. Zhang, M. Hohlmann, “Mechanical design and stress analysis of a large-area gas electron multiplier,” in preparation for submission to Journal of Mechanical Design (JMD). This work was presented at the 2017 Florida Academy of Sciences annual meeting and received an “Honorable Mention Undergraduate Oral Presentation” award.
A. Zhang and M. Hohlmann, "Accuracy of the geometric-mean method for determining spatial resolutions of tracking detectors in the presence of multiple Coulomb scattering," JINST 11 P06012 (2016), June 21, 2016.
A. Zhang, V. Bhopatkar, M. Hohlmann, et al., "R&D on GEM Detectors for Forward Tracking at a Future Electron-Ion Collider", Proc. of IEEE Nuclear Science Symposium 2015, San Diego, CA; arXiv:1511.07913, Nov 24, 2015.
A. Zhang, et al., "Performance of a large-area GEM Detector read out with wide radial zigzag strips," Nucl. Inst. Meth. A 811 (2016) 30-41, online version at ScienceDirect (18 Dec 2015).

## Slide 9
eRD6 Publication List: Breakdown per institute
INFN Trieste
N/A; Just Started
Stony Brook University:
M. Blatnik et al., “Performance of a Quintuple-GEM Based RICH Detector Prototype”, IEEE TRANSACTIONS ON NUCLEAR SCIENCE, VOL. 62, NO. 6, DECEMBER 2015.
M. Blatnik et al., “Performance of a Quintuple-GEM Based RICH Detector Prototype”, Nuclear Science Symposium Conference Record, 2015, IEEE
Manuscript in preparation: “First Results from a Prototype Combination TPC Cherenkov Detector with GEM Readout”, to be submitted to the IEEE Transaction on Nuclear Science in early 2017.
Proceedings in preparation: “First Results from a Prototype Combination TPC Cherenkov Detector with GEM Readout”, for the IEEE NSS/MIC 2016 in Strasbourg.
Univ. of Virginia
K. Gnanvo et al., “Performance in Test Beam of a Large-area and Light-weight GEM detector with 2D Stereo-Angle (U-V) Strip Readout”, Nucl. Inst. and Meth. A808 (2016), pp. 83-92. DOI: 10.1016/j.nima.2015.11.071
K. Gnanvo, et al. “Large Size GEM for Super Bigbite Spectrometer (SBS) Polarimeter for Hall A 12 GeV program at JLab”, Nucl. Inst. and Meth. A782, 77-86 (2015). DOI: 10.1016/j.nima.2015.02.017
Yale University
S. Aiola et al., “Combination of two Gas Electron Multipliers and a Micromegas as gain elements for a time projection chamber”, Nucl. Inst. and Meth. A834 (2016) 149-157.

## Slide 10
Backup

## Slide 11
Progress @ UVa: Optical & SEM Inspection of Chromium GEMs
SEM and FIB analysis of Cr-GEMs @ CERN (11/2017) to:
investigate Cr and Kapton etching?
Measure the thickness of the Cr layer
Samples from 4 GEM foils sent to CERN:
Cr-GEM1: damaged foil as 3rd GEM in proto I ⇨ high rate.
Cr-GEM2: 3rd GEM in proto II ⇨ long exposure
Cr-GEM3: 2nd GEM in 2 protos ⇨ high rate & long exposure
std-GEM: standard GEM foil with 5 µm electrode
Good foil (Cr-GEM3)
205.9 nm
Cross section of Cr-GEM hole and thickness of Cr layer
69.2 µm
Inner hole
Outer hole
Cr layer 2 × thicker than original assumption
52.8 µm
Cross section of a hole at the boundary between Cr and Cu

## Slide 12
eRD6 Consortium: What was achieved the past period
Brookhaven National Laboratory (BNL)
  Optimization of the zigzag pad readout pattern parameters, fabrication of PCB with this readout pattern and measurement of the position resolution
  Refining the analysis of the beam test results from TPC-C prototype, (in collaboration with SBU)
  Draft paper for submission to IEEE TNS
  Initial results from TPC gas studies
Florida Institute Of Technology (FIT)
  Inspection of the zigzag structure under a microscope of large readout board and HV test of the common GEM foil
  In-home production of the outer carbon fiber frames completed and mechanically tested and validated
  Manuscript on the performance of improved zigzag structures in preparation for NIM A
INFN Trieste
  Test of novel materials for the THGEM PCB
  Development of resistive MM by discrete elements with miniaturized pad size
Stony Brook University (SBU)
Procurement of all needed equipment for the upgrade of existing CsI evaporator
Preparation of the evaporation equipment to be installed into the evaporator
University Of Virginia (UVa)
Aging test of Cr-GEM with x-ray and validation of double zebra connection scheme on small GEM prototype
Finalize large U-V strips readout and zebra connection and support frame design.
Production of the board and the zebra connection pieces is ongoing at CERN.
Yale University
Hybrid Gain Structure for TPC read-out – 2 GEMs plus Micromegas (2-GEMs + MMG).
Multi-element stacked gated grid